## Slide 1: A Zero Trust Network with Automated Threat Detection and Response
BSC COMPUTER NETWORKS AND CYBER SECURITY · PROJECT PROPOSAL
using the Isolation Forest algorithm
Esborn Kihiu · Adm No. 168863
Supervisor: Mr. James Gikera
Strathmore University
School of Computing and Engineering Sciences
Notes: About 20 seconds. Good morning. My project is a Zero Trust network with automated threat detection and response, using the Isolation Forest algorithm. In the next ten minutes I will cover the concept, the literature, the design, how it is built, and how I prove that it works.

## Slide 2: Zero Trust that watches and acts
INTRODUCTION
Most networks trust a device once it is inside. An attacker or a misused account can then move freely, and signature tools miss behaviour they have not seen before.
Connect
A user plugs in a PC. The port stays closed.
Verify
An 802.1X login is checked by RADIUS.
Segment
The role picks the VLAN; ACLs allow only what it needs.
Detect
Isolation Forest scores every PC every 10 s.
Respond
Block, quarantine, disable or alert. No person needed.
Never trust, always verify, then keep watching what each device does and act on it.
Zero Trust network with automated threat detection · Esborn Kihiu
2 / 11
Notes: About 1 minute 10 seconds. The problem: most enterprise networks still trust a device once it is inside. If an attacker gets in, or a staff account is misused, little stops them moving between systems, and signature-based tools only catch attacks they already know. My concept combines Zero Trust with machine learning. Walk the picture left to right: a PC connects and the port stays closed. The user logs in with 802.1X and RADIUS checks the password. The user's role decides the VLAN, and ACLs allow only what that role needs. Once inside, the PC is still watched: every ten seconds its traffic is scored by an Isolation Forest. If it looks like an attack, the system responds by itself, using the same Zero Trust controls: block, quarantine, disable the account, or alert.

## Slide 3: Five technology areas the project draws on
LITERATURE REVIEW
Area | What the literature says | Used in this project
Networking | VLANs split one network into logical segments, and ACLs filter traffic between them (Baligodugula et al., 2024; Bredesen & Mujeye, 2025) | A VLAN per role; the ZT_POLICY ACL on the core switch
Systems | 802.1X with RADIUS gives AAA, and dynamic VLANs follow the user’s identity, not the port (Aramide, 2024; Islam & Dhanekula, 2023) | FreeRADIUS assigns VLAN 10, 20, 30 or 99
Cloud | Cloud and remote work blurred the perimeter, pushing firms to Zero Trust (Ahmadi, 2024); containers run real network software (Chen et al., 2025) | Containerlab runs real Arista switches in containers
Applications | Isolation Forest isolates unusual records in fewer random splits and needs no labelled attacks (Fuhnwi et al., 2023; Lakshmi et al., 2024) | Python and scikit-learn detector; Zabbix dashboard
Cybersecurity | Signature tools miss new behaviour (Rautaray, 2025); automating the first containment step shortens response (Jones, 2025) | Automatic block, quarantine and account disable
Gap: Zero Trust and ML detection are studied apart, and few working systems link detection to network controls (Falowo & Bou Abdo, 2026).
Zero Trust network with automated threat detection · Esborn Kihiu
3 / 11
Notes: About 1 minute 30 seconds. The review covers the five areas you asked for. Networking: VLANs and ACLs are the basic tools for segmentation. Systems: 802.1X with a RADIUS server gives authentication, authorization and accounting, and with dynamic VLAN assignment the VLAN follows the user, not the port. Cloud: cloud services and remote work removed the clear inside and outside, which is why organisations are moving to Zero Trust; container technology also lets me run real switch software on one machine. Applications: Isolation Forest is an unsupervised algorithm, so it does not need labelled attack data. Cybersecurity: signature tools miss new behaviour, and automating the first response shortens the time an attacker has. The gap: these are usually studied separately, and few working systems connect detection directly to the network controls. That is what this project does.

## Slide 4: Technical design: segments by identity
DESIGN AND ANALYSIS
Admin
VLAN 10
Staff
VLAN 20
Guest
VLAN 30
Quarantine
VLAN 99
Access switch
802.1X on every port; mirror port to the SIEM
Core switch
Routes the VLANs and enforces the ZT_POLICY ACL
Edge firewall
Linux iptables, default deny
DMZ web
10.10.40.0/24
Internet
through NAT
FreeRADIUS
who you are
SIEM host
what you do
Guests reach only the DMZ and internet · Quarantine reaches only RADIUS and the SIEM · The DMZ never opens a connection inward
Zero Trust network with automated threat detection · Esborn Kihiu
4 / 11
Notes: About 1 minute. This is the technical design. Every user sits in a VLAN chosen by their role: admin VLAN 10, staff VLAN 20, guest VLAN 30, and VLAN 99 for a quarantined host. All users connect through the access switch, which runs 802.1X on every port and asks FreeRADIUS who the user is. The core switch routes between the VLANs, and the ZT_POLICY access list enforces least privilege. The edge firewall is default deny and protects the inside from the DMZ web server and the internet. The access switch also copies all user traffic to the SIEM host, which is where detection runs. So RADIUS answers who you are, and the SIEM answers what you are doing. The policy line at the bottom is the analysis of who may reach what.

## Slide 5: Signalling: 802.1X login and VLAN
DESIGN AND ANALYSIS
Staff PC
Access switch
FreeRADIUS
1 · EAPOL-Start
2 · EAP-Request: Identity
3 · EAP-Response: “alice”
4 · RADIUS Access-Request
5 · PEAP tunnel: password checked
6 · Access-Accept + VLAN 20
7 · EAP-Success: port opens in VLAN 20
Zero Trust network with automated threat detection · Esborn Kihiu
5 / 11
Notes: About 1 minute. The first signalling diagram is the 802.1X login, which is the identity half of Zero Trust. The PC starts with EAPOL-Start. The switch asks for an identity, and the PC answers with the username, here alice. The switch forwards it to FreeRADIUS in an Access-Request. Inside a PEAP tunnel the password is checked. If it is correct, RADIUS sends Access-Accept with a VLAN attribute, the Tunnel-Private-Group-Id, set to 20 for staff. The switch then opens the port in VLAN 20. If the password is wrong, RADIUS sends Access-Reject and the port stays closed, so no traffic gets through before a login.

## Slide 6: Signalling: detect and quarantine
DESIGN AND ANALYSIS
Guest PC
Access switch
SIEM detector
FreeRADIUS
Zabbix
1 · Scan: 10+ ports
2 · Mirror copy
3 · Flagged: port scan
4 · Rule: VLAN 99
5 · SSH: bounce port
6 · 802.1X login again
7 · Accept: VLAN 99
8 · Alert + email
Zero Trust network with automated threat detection · Esborn Kihiu
6 / 11
Notes: About 1 minute. The second signalling diagram shows detection and response, using a port scan from the guest PC as the example. One: the guest PC probes ten or more ports. Two: the access switch mirrors that traffic to the SIEM host. Three: at the end of the ten-second window the Python pipeline builds eight features, the Isolation Forest scores the window as an anomaly, and the classifier names it a port scan. Four: the response engine writes a rule into FreeRADIUS that puts this user in VLAN 99. Five: it logs in to the access switch over SSH with Netmiko and bounces the port. Six and seven: the PC logs in again and RADIUS now places it in quarantine VLAN 99. Eight: the event goes to Zabbix, which raises an alert and emails the administrator. The other attacks follow the same pattern with a different action: a DoS source is blocked by a deny line in the core ACL, and an insider has the account disabled.

## Slide 7: Real systems and software
IMPLEMENTATION
Part | Software | What it does
Lab platform | Containerlab on Kali Linux | Builds the whole network on one laptop
Switches | Arista cEOS 4.36 (core, access) | VLANs, 802.1X, ACL, mirror port
Identity | FreeRADIUS 3.0 with PEAP | Checks logins, returns the VLAN
Edge and DMZ | Linux with iptables; web server | Default-deny firewall and DMZ
Detection | Python, pandas, scikit-learn | Isolation Forest on 8 features per PC
Response | Python with Netmiko (SSH) | Block, quarantine, disable, alert
Monitoring | Zabbix with email alerts | Dashboard of scores and actions
Packet Tracer was ruled out: it gives no real packets for detection and no SSH for Python to act on.
Zero Trust network with automated threat detection · Esborn Kihiu
7 / 11
Notes: About 1 minute. These are the actual systems. Everything runs in Containerlab on one Kali Linux laptop, and the whole lab is rebuilt with one command. The two switches run real Arista EOS software, so they behave like production switches. FreeRADIUS does the 802.1X logins with PEAP and returns the VLAN. The edge is a Linux router with an iptables default-deny firewall and a DMZ web server. Detection is Python with pandas and scikit-learn. The response engine uses Netmiko to log in to the switches over SSH. Zabbix gives the dashboard and emails alerts. I chose real software over Packet Tracer because Packet Tracer gives no real packets for the detector and Python cannot log in to it to apply a response.

## Slide 8: System architecture
IMPLEMENTATION
Zero Trust network · Containerlab
Access switch
Core switch
FreeRADIUS
Edge firewall
DMZ web server
Admin, staff and guest PCs
Mirror port: a copy of all user traffic
Actions: SSH to switches, RADIUS rules
Detection and response · Python on the SIEM host
Collector
Raw socket on the mirror
Features
8 numbers per PC every 10 s
Isolation Forest
Score, plus a brute-force rule
Classifier
Names the attack type
Response engine
Block, quarantine, disable
Zabbix
Dashboard and email
Zero Trust network with automated threat detection · Esborn Kihiu
8 / 11
Notes: About 1 minute. This is the system architecture in two layers. The top layer is the Zero Trust network in Containerlab: the switches, FreeRADIUS, the edge firewall, the DMZ and the user PCs. The access switch mirrors all user traffic down to the SIEM host. There, a Python pipeline runs left to right: the collector reads packets from the mirror port, the feature builder turns each PC's traffic into eight numbers every ten seconds, the Isolation Forest scores the window, with one extra rule for repeated failed logins, the classifier names the attack type, and the response engine acts. The actions go back up to the network: SSH commands to the switches, and rules in FreeRADIUS. Every score and action is also sent to Zabbix for the dashboard and email alerts.

## Slide 9: How I prove that it works
EVALUATION
Test | What it shows
Policy checks | Each role reaches only what it should; run after every rebuild
802.1X logins | Right password: right VLAN. Wrong password: port stays closed
Detector | 594 normal and 100 attack windows; 5-fold cross-validation
End to end | 5 live attacks; time from window end to the action
Measured by accuracy, detection rate, false-alarm rate, F1-score and response time. Labels are used only to score the results.
99%
accuracy over all test windows
100%
of 100 attack windows detected
1.1%
false alarms, which only alert
<2 s
from detection to action
Zero Trust network with automated threat detection · Esborn Kihiu
9 / 11
Notes: About 1 minute 15 seconds. I prove the system works with four kinds of test. First, policy checks: after every rebuild a script confirms that each role can reach only what it should, for example a guest can reach the DMZ web server but not a staff PC. Second, 802.1X: the right password lands the user in the right VLAN, and a wrong password leaves the port closed. Third, the detector: 594 normal windows and 100 attack windows, five attack types at five intensities, scored with five-fold leave-one-run-out cross-validation so every run is tested by a model that never saw it. Fourth, end to end: each attack is launched live while the other PCs work normally, and I time how long it takes from the end of the window to the action. The results on the right: 99 percent accuracy, every attack window detected, 1.1 percent false alarms, which only raise an alert and never block a user, and under two seconds from detection to action. The final rehearsal on 16 GB answered all five attacks in 1.1 to 1.9 seconds.

## Slide 10: Limitations of the implementation
EVALUATION
Simulated traffic
Scripted users are more regular than real ones, so a real network would see more false alarms.
Simulated night-time
Off-hours activity is marked by a flag, not observed at night.
Small lab
One access switch and three users, all on one laptop with 16 GB of RAM.
Known attack types
Only five attacks were tested; others, such as lateral movement over SSH, were not.
Next: compare with autoencoders and One-Class SVM (Syzranova et al., 2026), and link alerts to a SOAR or ticketing platform (Kumar et al., 2025).
Zero Trust network with automated threat detection · Esborn Kihiu
10 / 11
Notes: About 45 seconds. These are the limitations. All traffic is generated by scripts, which are more regular than real people, so the false-alarm rate on a real network would likely be higher. Night-time is simulated with a flag. The lab is small: one access switch, three users, and one laptop. And only the five attack types in scope were tested. To reduce the risk of a false alarm cutting someone off, unclear cases only raise an alert, and every action can be reversed. Future work is to compare Isolation Forest with other unsupervised models and to connect the response engine to a SOAR or ticketing platform.

## Slide 11: Questions?
THANK YOU
A Zero Trust network that verifies every login, watches every device, and responds by itself in under two seconds.
Esborn Kihiu · Adm No. 168863 · Supervisor: Mr. James Gikera
Notes: About 10 seconds. To sum up: the network verifies every login, watches what every device does, and responds by itself within two seconds. Thank you. I am happy to take your questions.